## Slide 1
Exam: Mathematical Optimization
Analysis and results reproduction of:
Dynamic Wireless Charging Lanes location model in urban networks considering route choices
Cong Quoc Tran, Mehdi Keyvan-Ekbatani, Dong Ngoduy, David Watling
Transportation Research Part C
2022
Giorgia Leoncilli, Sara Serafino

## Slide 2
To support the system planner in deploying the WCL, the paper takes into consideration traffic dynamics and congestion under multiple vehicle classes (EV and ICV).
The problem combines a mixed-integer linear program with dynamic routing behaviour into the charging location problem.
The objective is to maximise network performance while providing insights into traffic propagation patterns over the network.
To determine the optimal location for dynamic Wireless Charging Lanes

## Slide 3
Network design problem → limited to single Origin-Destination networks
Upper level: minimise the system cost with specific demands
Lower level: Traffic Assignment Problem

## Slide 4
Traffic Assignment Problem
Determine which routes will be used and how much traffic can be expected on each route.
Requirements:
Estimated n.vehicles
Available routes and travel times on each route
Decision criteria for route choice (route choice behaviours and path feasibility constraints)
Route choice decisions are a function of travel times
Travel times are determined by traffic flow
Traffic flow is a product of route choice decisions

## Slide 5
Traffic Assignment Problem with Dynamic System Optimal
User Equilibrium:
Users choose the route that minimizes their own travel time.
System Optimal:
Users cooperatively achieve the minimum system-wide travel time.
✅ REALISTIC SCENARIO
❌ EFFICIENT IN THE
BI-LEVEL FRAMEWORK
❌ REALISTIC SCENARIO
✅ EFFICIENT IN THE
BI-LEVEL FRAMEWORK

## Slide 6
Traffic Assignment Problem with Dynamic System Optimal
User Equilibrium:
Users choose the route that minimizes their own travel time.
Problem reformulated as single-level
System Optimal:
Users cooperatively achieve the minimum system-wide travel time.
✅ REALISTIC SCENARIO
❌ EFFICIENT IN THE
BI-LEVEL FRAMEWORK
❌ REALISTIC SCENARIO
✅ EFFICIENT IN THE
BI-LEVEL FRAMEWORK

## Slide 7
Assumptions
All EVs have homogeneous battery size.
The energy consumption rate of an EV is assumed proportional only to the travelled distance and homogeneous for all EVs.
The energy recharge rate is underestimated proportionally to travel time at free-flow speed.
Network must be cleared at time horizon.

## Slide 8
General formulation
Variables:
if link has WCL
if path is feasible
state of energy of an EV after traversing link on path
number of vehicles class on link at time
incoming traffic flow of vehicles class to link at time
outgoing traffic flow of vehicles class from link at time
upstream traffic of vehicles class from link to link at time
Parameters:
budget
demand rate of vehicles of class (vehicles/timestep)
free-flow speed (m/min)
backward speed (m/min)
jam density (vehicles/m)
maximum flow capacity speed (vehicles/min)
aggregate link-based share factor of vehicles of class

## Slide 9
Constraints
initial state of energy
budget
Recharge:
energy received
travel time at velocity
path feasibility
Consumption:
consumption rate
length of link
Sets:
P = paths
E = links, including source links (ER),
sink links (ES) and normal links (EA)
incoming/outgoing links to/from link

## Slide 10
Constraints
incoming flow ≤ vehicles on
vehicles conservation
capacity per class
demand for incoming vehicles at origin
network cleared at destination
flow conservation
}

## Slide 11
Constraints
incoming flow ≤ vehicles on
vehicles conservation
It can be used to give priority to one vehicle class over the other
capacity per class
demand for incoming vehicles at origin
network cleared at destination
flow conservation
}

## Slide 12
Constraints
incoming flow ≤ vehicles on
vehicles conservation
It can be used to give priority to one vehicle class over the other
capacity per class
demand for incoming vehicles at origin
network cleared at destination
flow conservation
}
Not coherent with assumption of network cleared at time horizon

## Slide 13
Constraints
supply
different route choices
true capacity
}
demand
(veh/min) → (veh/timestep)

## Slide 14
Objective function
Set of discrete time steps
Penalty cost to incentivise travellers to move along instead of waiting
Maximising total traffic outflow is mathematically equivalent to minimising total travel times.

## Slide 15
Minimising constraints

## Slide 16
Modified demand rate at origin
Clearance time in worst case scenario:
Exit capacity of sink link per timestep
n.vehicles entering each timestep
Last time step to clear network

## Slide 17
Extra constraint
To avoid conflict with constraint 19
impose a minimum upstream traffic for feasible paths.
Otherwise if there is too much congestion, constraint 19 makes even if feasible.
Arbitrary small
( )

## Slide 18
Gurobi optimization: increasing dimensionality
Boosting the dimensionality of the problem, the time of execution highly increases.
Dimensionality increases

## Slide 19
Increasing time horizon increases execution time
With increasing timestep, less vehicles enter the network, lowering the execution time
Parameters value’s effect on execution time

## Slide 20
Direct proportionality between and , , , highlighting a peak congestion at given values.
Parameters value’s effect on execution time

## Slide 21
Direct proportionality as expected
Number of variables and constraints VS dimensionality

## Slide 22: Thank you for the attention

## Slide 23
Sitography
Implemented paper: «Dynamic wireless charging lanes location model in urban networks considering route choices», Tran et al., 2022, https://www.sciencedirect.com/science/article/pii/S0968090X2200095X
Cited paper for : «Multiclass dynamic system optimum solution for mixed traffic of human-driven and automated vehicles considering physical queues», Ngoduy et al., 202,1 https://www.sciencedirect.com/science/article/pii/S0191261521000011
Traffic Assignment Problem: lecture 4 of «Principles of Transportation Engineering» at the Iowa State University, https://www.youtube.com/watch?v=qjSLM3-ENxU